## Slide 1
RESEARCH IDEA
Can one EEG channel
classify sleep stages?
A reproducible deep-learning pipeline for
automatic sleep staging
SINGLE-CHANNEL EEG
5 SLEEP STAGES
30-SECOND EPOCHS
A simpler input, a transparent evaluation,
and a research-ready prototype.
FROM ONE SIGNAL
EEG
Fpz-Cz
Wake
N1
N2
N3
REM
one 30-second epoch
Concept inspired by recent single-channel EEG sleep-staging research
01 / 04
Notes: Hello everyone. My project is about automatic sleep stage classification from EEG.
The key idea is to investigate whether one EEG channel can provide enough information to classify five sleep stages automatically.
[Sources]
- https://www.nature.com/articles/s41598-026-62832-5
- https://physionet.org/content/sleep-edfx/1.0.0/

## Slide 2
The research idea is focused and testable
Reduce the input, preserve the signal information, and evaluate generalization.
CORE QUESTION
Can one channel
support reliable
sleep staging?
without relying on a
full multi-sensor PSG setup
PROJECT OBJECTIVES
01
Build
A single-channel EEG sleep-staging pipeline
02
Compare
Baseline CNN vs. the full representation + sequence model
03
Evaluate
Class imbalance, unseen subjects, and per-stage performance
Research prototype — not a medical diagnostic device
Research objective: reproducible modeling and honest evaluation
02 / 04
Notes: The core idea is simple: take a 30-second segment of single-channel EEG, learn its time-frequency patterns, and predict one of five sleep stages.
The project objectives are to build the pipeline, compare model components, and evaluate generalization to unseen subjects.
[Sources]
- https://www.nature.com/articles/s41598-026-62832-5
- https://physionet.org/content/sleep-edfx/1.0.0/

## Slide 3
The proposed workflow turns EEG into five labels
Each step has a specific role: normalize, represent, learn, and classify.
30s EEG
Fpz-Cz
3,000 samples
Normalize
clean
and scale
SST map
T–F
map
CNN
local
features
Contrastive
robust
features
GRU × 2
ordered
context
5 stages
Wake · N1
N2 · N3 · REM
WHY THIS COMBINATION?
SST preserves time–frequency detail.
CNN learns local patterns. GRU preserves the order of feature windows.
PRIMARY METRIC
Macro-F1 + per-stage F1
because the classes are imbalanced
Model structure adapted from the selected recent research protocol
03 / 04
Notes: The workflow begins with a 30-second Fpz-Cz epoch, normalizes the signal, creates a time-frequency representation, and learns features with CNN.
Contrastive learning improves robustness, and a two-layer GRU processes the ordered feature windows before predicting the five labels.
Macro-F1 is the primary metric because the classes are imbalanced.
[Sources]
- https://www.nature.com/articles/s41598-026-62832-5
- https://physionet.org/content/sleep-edfx/1.0.0/

## Slide 4
Data, evaluation, and expected contribution
The proposal ends with a reproducible experiment, not only a model score.
DATASET
Sleep-EDF Expanded
197 whole-night PSG recordings
EEG + expert-scored hypnograms
Input
Fpz-Cz EEG
Labels
Wake / N1 / N2 / N3 / REM
Split
subject-wise train / test
EVALUATION PLAN
01
Baseline
Majority class + CNN
02
Ablation
SST / contrastive / GRU / class weighting
03
Metrics
Accuracy, macro-F1, kappa, confusion matrix
04
Generalization
Unseen subjects, then external dataset
EXPECTED CONTRIBUTION: a transparent, reproducible single-channel EEG sleep-staging pipeline
Dataset: PhysioNet Sleep-EDF · evaluation designed for reproducibility
04 / 04
Notes: The primary dataset will be Sleep-EDF Expanded, which contains whole-night polysomnography recordings and expert-scored hypnograms.
The final experiment will use subject-wise splits, compare baselines and ablations, and report both overall and per-stage metrics.
The expected contribution is a reproducible research pipeline and an honest analysis of generalization.
[Sources]
- https://physionet.org/content/sleep-edfx/1.0.0/
- https://www.nature.com/articles/s41598-026-62832-5